## Slide 1: AuthedIP Overview
Daniel Chin. 3/15/2022.

## Slide 2: Background: Transport/Application-layer vs Network-layer security
App-layer threats:
  Eavesdropping on communication.
  Intercepting and changing packet content.
App-layer solution: Encrypt your traffic!
  This is necessary, but not enough.
Net-layer threats:
  Resource depletion attacks: DoS.
  Eavesdropping on traffic volume over time about each (source, dest) pair.

## Slide 3: A security problem with Ethane
User -?- MAC addr – IP addr
  Blind to: Multi-user endhost.
  The core problem: No per-packet user verification!
Packet – first Ethane router ingress port -?- MAC addr – IP addr
  Blind to: MAC spoofing.
  The core problem: No per-packet user verification!

## Slide 4: AuthedIP
Do per-packet user verification!
Goal: only authenticated packets are allowed in the network.
  If you are not a registered user, you can’t send anything.
  If you are a registered user, you can’t send anonymous packets.
Putting the check inside the network prevents DoS.
  Compare: check at receiver.
No anonymity: anomalies can be traced back to registered users.

## Slide 5: Background: RSA signature
I have RSA key pair: public key + private key .
I keep my private key secret, and announce my public key .
To sign a message, I apply my private key:
Other people can verify using my public key:
Two facts:
  If you don’t have it’s hard to generated a that will pass the verification.
  Observing many pairs of usually does not give away.

## Slide 6: AuthedIP: The idea
Each user is registered with Controller.
  i.e. Controller has a list of public keys of all users.
Each IP packet is signed by a user.
Routers reject packets that fail verification.
Simple!!! Right?

## Slide 7: Attack 1: steal verified packet and change dest
I listen on the Ethernet and record a packet sent by someone else.
I can change the destination address. Send it.
The packet will not be rejected.
Imagine:
  Jessica sent “clear database” to the test database. I send her packet to the production database.
Solution: Sign not only the payload, but also source-destination addresses.

## Slide 8: Attack 2: record and playback
I record a packet, do not modify it, and send it back into the net.
Solution: Have a timestamp in each packet, and sign the timestamp too.

## Slide 9: AuthedIP packet
h = hash(source, dest, content)
t = timestamp()
s = sign(concat(t, h))
Verify:
  The hash is correct.
  The signature is correct.
  The timestamp is fresh.
  The public key is registered.

## Slide 10: AuthedIP packet
h = hash(source, dest, content)
t = timestamp()
s = sign(concat(t, h))
This can be IP-compatible! If you put in the payload of IP.
  Question: will headers work?

## Slide 11: Attack 3: duplicate recent packets to DoS
Stays within the freshness constraint.
I can’t think of a solution yet…

## Slide 12: Performance!
Forward
Verify
Time

## Slide 13: Performance!
Forward
Verify
Time

## Slide 14: Performance!
Wait.. So why should the routers do the verifications?
Just duplicate the packets to verifier servers.

## Slide 15: General design
Controller
Verifier server

## Slide 16: Project Repo
https://github.com/Daniel-Chin/AuthedIP
Aims at defining the complete behaviors with Python code.